MIMO in Wireless Networking

Abstract

To cater to the 4G service demands and ever growing requirements of today’s mobile networks, we need a technology that helps achieve considerable throughput and improve cellular coverage. All systems are attempting to achieve high data transmission rates nearing 1 Gb/s and provide high speed without compromising good quality of service (QoS). High data rate refers to achieving channel capacity and quality for minimizing the probability of error (Pe). A single-input single-output (SISO) system uses one antenna at both the transmitter and receiver for radio transmissions, which consist of an rf chain. To increase throughput in a radio link, many antennas are placed at both the transmitter and receiver. In other words, the link will have multiple rf chains. This method is known as multiple-input multiple-output (MIMO). MIMO technology uses multiple radios to transfer more data simultaneously. MIMO will prove helpful in long term evolution (LTE) as it helps transfer more data at the same time. Each antenna has a dedicated rf chain in MIMO so that many rf chains can coexist. MIMO systems operate in two modes, namely spatial multiplexing gain and diversity coding. Multiple spatial streams, i.e., radio signals are simultaneously sent on a single frequency in spatial multiplexing. Here a signal is split into multiple signals, and these multiple data streams are transmitted from different transmitting antennas in the same frequency channel. At the receiver, these data are separated into parallel channels if the signals arrive with different profiles. In diversity coding, we consider a single stream of data that are encoded separately and differently using a technique called space-time coding and then transmitted from each of the many transmitting antennas. This enables data exchange to be nearly twice at a given time when compared with SISO and improves coverage within a cell. Hence, this technology plays an important role in 4G protocols such as LTE for providing better cell coverage and higher capacity for a given cell.

# Comments

Word choice:

Choosing the right word to convey meaning eases readability and understanding. “Cater” is a more appropriate word in this context.

Typographical error:

The spelling error has been corrected here.

Style:

In academic writing, when the value is expressed in numerals, the abbreviation of the corresponding unit should be used.

Word choice:

Choosing the right words to convey meaning enhances readability and understanding.

Style:

Generally, the abbreviations need to be defined at the first instance in both the abstract and the text.

Language:

In academic writing, information is presented with accuracy and conciseness. Formal, precise language is a hallmark of academic English.

Grammar:

The plural verb “are” is used as it agrees with the plural noun “antennas.”

Attention to detail:

“rf” has been lowercased for consistency.

Style:

In American English, the nonrestrictive clause is mostly introduced with the relative pronoun “that.”

Grammar:

The adverb has been appropriately placed for fluent readability.

Punctuation:

Because “hence” is the introductory phrase here, a comma must be inserted.